Efficiency of Power Station

A power station is combination of many parts. For a coal based thermal plant, the components are the boiler, the steam turbine, the generator and the transformer. The efficiency of power stations is the combination of all the parts. For example, if the efficiencies of the boiler, the steam turbine, the generator and the transformer are 50%, 95%, 97% and 99% respectively, then the final efficiency of the power station is 50%x95%x97%x99% = 45.6%.