Resistance

- What is the Voltage across a 14 Ω Resistor which is carrying a Current of 7 A?

- Calculate the Voltage across a 2 Ω Resistor which is carrying a Current of 10 A.

- What Current will flow through a 150 Ω Resistor that is connected across a 3 V Battery?

- What Current will flow through a 5 Ω Resistor when connected across a 2 V Power Supply?

- What is the Resistance of a car starter motor which draws a Current of 48 A from a 12 V Battery?

- Calculate the Resistance of a 240 V light globe if it draws a Current of 1.5 A.

- What is the Voltage across a torch bulb if the Resistance is 3 Ω while the Current drawn is 2A?

- Find the Resistance of an electric kettle that draws 12 A while a Voltage of 240 V is applied.

- (Extension) Calculate the Current flowing through a light bulb that has a Resistance of 250 mΩ while the Voltage is 5 V.

- (Extension) A 12 V car Battery has to supply a Current of 30 A to a starter motor through a cable of Resistance 0.01 Ω Calculate the Voltage that will appear across the starter motor.

Resistance

Answers:

- 98 V

- 20 V

- 0.02 A

- 0.4 A

- 0.25 Ω

- 160 Ω

- 6 V

- 20 Ω

- 20 A

- 11.7 V